## Slide 1
1
Locomotion Is a Control Problem
THE PROBLEM
Position-based locomotion is accurate under known conditions but rigid — it struggles with compliance, disturbance handling, unknown terrain, and the sim-to-real gap.
→ Torque-based control may enable more compliant interaction and improve adaptation capability.
POSITION CONTROL
TORQUE CONTROL
Command position
Command force
▼
▼
Rigid behavior
Compliant interaction
▼
▼
Poor adaptation
Adaptive response
RESEARCH QUESTION
How can robots achieve safer and more adaptive locomotion in unknown environments?
Adaptive behavior ≠ adaptive control
Refs SATA · Chen et al. (torque control) · Lee et al. (terrain) · Miki et al. (perceptive loco.)
Notes: [~40 sec] CORE MESSAGE (repeat across the talk): We are NOT proposing a new controller. We aim to reproduce SATA, understand its adaptive behavior, and discuss it from a control perspective. TALKING POINTS: - Frame this as a CONTROL problem, not an RL talk. - Position control commands a joint angle; a low-level PD loop turns the error into torque. Stiff and accurate when the world is known. - It fails on exactly what this course cares about: compliance, disturbance rejection, unknown terrain, sim-to-real gap. - Torque control commands force directly, so the robot can yield and adapt instead of resisting. TRANSITION: 'The question is how to get adaptive locomotion in unknown environments — SATA is one bio-inspired answer.'

## Slide 2
2
SATA: Bio-inspired Adaptation in Torque Control
An RL torque policy wrapped by a biomechanical layer and a growth curriculum.
Observation
▼
Torque Policy (RL)
▼
Biomechanical Layer
▼
Torque Output
▼
Robot
State feedback
(base + fatigue)
M
Biomechanical Model
activation · muscle · fatigue
G
Growth Mechanism
torque limit · training curriculum · control frequency
Goal: smooth, safe torques that progressively unlock capability — demonstrated zero-shot deployment (sim-to-real).
Refs SATA · Hill (muscle dynamics) · Liu et al. (fatigue) · Bellegarda & Ijspeert (CPG-RL)
Notes: [~60 sec] TALKING POINTS: - One message: SATA injects bio-inspired adaptation INTO a torque policy. Don't read equations. - Flow: observation -> RL torque policy -> biomechanical layer -> torque -> robot; fatigue state feeds back. - Biomechanical model: activation smooths the command, a muscle model prevents abrupt torque, fatigue discourages overusing joints. - Growth mechanism: torque limit, reward, and control frequency unlock progressively — like an animal maturing. - Net effect: safe torques plus generalization, deployed zero-shot. TRANSITION: 'That's what SATA is — here is how WE plan to study it.'

## Slide 3
3
Plan: Understand → Reproduce → Analyze
A feasible 3-phase study — we interpret SATA, we do not redesign the RL.
1
PHASE 1
Reproduce
Set up Isaac Gym on a CUDA server (container / venv) and run the official SATA training.
OUTPUT simulation running
→
2
PHASE 2
Ablation
Disable fatigue · change torque limit · modify growth schedule · vary terrain.
OUTPUT behavioral data
→
3
PHASE 3
Adaptive Interpretation
Growth ↔ gain scheduling
Fatigue ↔ internal feedback
Torque limit ↔ adaptive constraint
(analogies, not claims)
OUTPUT analysis & discussion
→
4
PHASE 4 · OPTIONAL
Residual Compensation
Preliminary exploration.
τ_total = τ_SATA + τ_comp
Only if time & feasibility allow.
OUTPUT preliminary observations
APPROACH
We analyze adaptation instead of proposing new methods — we do not redesign the RL algorithm.
Refs SATA · RL2AC · DecAP
Notes: [~50 sec] TALKING POINTS: - Feasibility is the point of this slide: executable, not just a paper review. - Phase 1: stand up the official SATA pipeline in Isaac Gym — proves we can run it. - Phase 2: controlled ablations — toggle fatigue, retune torque limit / growth, change terrain; observe behavior shifts. - Phase 3: map each mechanism to an adaptive-control reading (analogy, not equivalence). - Phase 4 residual term only if time allows — not promised. TRANSITION: 'So what do we expect to deliver?'

## Slide 4
4
Expected Contribution
We study adaptive behavior — not propose a new RL algorithm.
EXPECTED OUTPUTS
1
Simulation reproduction
2
Behavior analysis (ablation)
3
Adaptive-control interpretation
4
Literature-grounded discussion
RESEARCH QUESTIONS
RQ1
Why torque control?
RQ2
What creates adaptation?
RQ3
How does it relate to adaptive control?
RQ4
Can lightweight compensation help?
IN ONE LINE
This project investigates how bio-inspired torque control creates adaptive locomotion behaviors, and interprets these mechanisms through adaptive and robust control perspectives.
Notes: [~30 sec] TALKING POINTS: - Close the loop, no overclaiming: the contribution is understanding, not a new algorithm. - Three concrete outputs: reproduction, behavior analysis, control-theoretic interpretation. - The four research questions map onto the four slides. CLOSING LINE (read the bottom band): bio-inspired torque control -> adaptive behavior -> interpreted through adaptive & robust control. REINFORCE THE CORE: we are not proposing a new controller — reproduce SATA, understand its adaptive behavior, discuss it from a control perspective. TRANSITION: 'Happy to take questions.'